Open Source Cell Top Battery Management System – OSCTBMS

# Inter-module communications

On the top of each cell is a monitor unit that measures the voltage and temperature of the cell. Additionally, it has a load that can be turned on or off to balance the cells.
The cell top monitors have to report their information to the charger manager.
The messages are built around a 4 byte data packet – forward error correction expands this to 6 bytes when the data is actually transmitted. The first 2 bytes are used for the cell voltage in mV and the second 2 bytes are used for the cell temperature in 1/10ths of a degree Celsius.

Cell mV	0 – 4200	0x1068	13bits required
Cell Temperature	0 – 1000	0x3E8	10bits required

The state of the load is encoded in the msb of the voltage bytes, the next 2 bits are always zero.
The upper 3 bits of the temperature bytes are used for the 3 alarm indicators.

Byte 1
Byte 2
Byte 3
Byte 4
l
t
v
u
Load status bit
Overtemperature alarm bit
Over-voltage alarm bit
Under-voltage alarm bit

0
0

The charger controller needs to be able to initiate the sending of cell data so it can control the sampling rate for logging etc. The charge controller should also be able to activate individual cell loads.
The initiator message from the charge controller is identified by having bits 1, 2 and 3 both set to 1 in the temperature pairs of bytes. This can NEVER occur with cell data as it would mean over-voltage AND under-voltage at the same time.

Byte 1
Byte 2
Byte 3
Byte 4
1
1
1
x
0
0