Open Source Cell Top Battery Management System – OSCTBMS
# This project came about because we were so offended by what was available at the time. Commercial systems were overly complex and hideously expensive and the open source offerings were quite badly designed with minimal heat-sinking and poor track layout.
# Our original intention was to provide all the data so that hobbyists could make their own and so it was designed with 0805 resistors that were easier to hand place with a pair of tweezers. We later decided that with our volume buying and machine placement we could sell ready made units at cost which would be way below what a hobbyist could buy the parts for so now the boards use 0603 components and are 100% surface mount.
# Concept
The BMS consists of 2 main components, the cell top monitor bolted directly onto the top of the prismatic cell and the Battery Manager which communicates with all the cell top monitors, correlates the information and controls the charger as well as providing state-of charge (SoC) etc information.
Since the cells are wired in series there only needs to be 1 current sensor so that is with the Battery Manager, the Cell Top Monitors measure the voltage at the terminals and the temperature. For cell balancing they provide a load which uses the battery terminal as a heat-sink – the opposite terminal to where the temperature is measured.
# Inter-module communications

The cell top monitors have to report their information to the Battery Manager, in return they need to be told the mean cell voltage in order to know when to activate their individual loads.
The messages are built around a 4 byte data packet – forward error correction expands this to 6 bytes when the data is actually transmitted. The first 2 bytes are used for the cell voltage in mV and the second 2 bytes are used for the cell temperature in 1/10ths of a degree Celcius.

Cell mV	0 – 4200	0x1068	13bits required
Cell Temperature	0 – 1000	0x3E8	10bits required

The state of the load is encoded in the msb of the voltage bytes.
The upper 3 bits of the temperature bytes are used for the 3 alarm indicators.

Byte 1
Byte 2
Byte 3
Byte 4
l
t
v
u
Load status bit
Overtemperature alarm bit
Over-voltage alarm bit
Under-voltage alarm bit

The mean cell voltage message from the charge controller is identified by having bits 2 and 3 both set to 1 in both pairs of bytes.

Byte 1
Byte 2
Byte 3
Byte 4
0
1
1
0
1
1

## Transmission time
A 6 byte block of data needs to be transmitted for each cell.

baudrate	1 cell	16 cells (48v pack)
4800	12.5ms	200ms
9600	6.25ms	100ms
19200	3.125ms	50ms